## Slide 1: Korean Lake Ecological Observatory Network
Buyoung Ahn, Youngjin Kim, Jongsuk Lee and Kum Won Cho
Dept. of Cyber Environment Development, KISTI
Bumcheol Kim
Dept. of Environmental Science,
Kangwon National University

## Slide 2
Goal
Organization
Roles of KISTI and KNU
Ecosystem Monitoring Testbed
Installing Sensor Network
Sensors in Lake Soyang and Lake Euiam
Expected Effect of KLEON
Content

## Slide 3
Establishment of ecological observatory network in lakes and rivers
1. Goal of KLEON
Construction of KLEON (Korean Lake/Reservoir Ecological Observation Network)
Supporting Global Joint Ecology
Research Environment
Sharing Ecology
Observation/ Information
Using Result for
Environment Preservation Policy
/Teaching Resource
Global Joint Research
Environment/Ecology analysis
Construction of Observation Infrastructure
Summary, Analysis and Prediction
of Observation
Data Standardization
Visualization
Simulation Model
Data Convergence
Computing Resource
High performance Network
large-capacity Storage
KISTI Cyber Infrastructure
KLEON
(Web)

## Slide 4
Collection of Global Lake/Reservoir Observation Data
Construction of Global Joint Research Network
  With Global e-Science Gateway
2. Organization of KLEON
Using Result for Environment Preservation Policy /Teaching Resource
Supporting Global Joint Ecology
Research Environment
Ecology
model
KLEON testbed
Visualization
Data
convergence
Data
standardization
Request of data, information
Requested data, information
Observation
Web Service
Request of data, information
Requested data, information
Sharing Ecology
Observation/ Information
Domestic observation
(Lake Soyang, Lake Uiam,
Han river, Swamp Upo)
Global Observation
(USA, New Zealand, Thailand)
Computing
Resource
High performance
network
Large-capacity
storage
KISTI Cyber infrastructure
Simulation
model
Ecologist/Statistician
(KNU, CNU)
Ecosystem
assessment
Simulation
modeling
Data analysis &
prediction
Data analysis
& prediction
Information
/Knowledge
Raw/meta
data
Analyzed
data
User query
processor

## Slide 5
3. Roles of KISTI and KNU
Kangwon National University | Dept. of Cyber Environment Development of KISTI
Building Web portal Real time sensor data (High frequency) Provide the observation data Construction of sensor network Lake (Soyang, Uiam) Swamp Upo River (Han, Anyang, Soyang) Global Cooperation GLEON, KEON Application Water quality modeling using CE-QUAL-W2 | Supporting IT Infrastructure Server, Large-capacity storage, High performance network Constructing the database for sensor data management Raw data for 30 years Metadata(standardization, share) Developing GUI interface Simulation model presentation based on Google earth Global Cooperation & IT support GLEON, KEON Survey of IT Techniques for Ecosystem CUAHSI (Consortium of Universities for the Advancement of Hydrologic Science) GLEON (Global Lake Ecological Observatory Network) OGC (Open Geospatial Consortium)

## Slide 6
Testbed for monitoring ecosystem in Lakes and Reservoirs
  Install sensors such as water temperature, DO, turbidity
  Real time observed data management
Sensors
  Water temperature, Electrical Conductivity, Dissolved Oxygen, pH, Turbidity
Sensor management
  Clean and measurement adjustment per every week
Real time sensor data transmission for monitoring three sites
  Storing the real time data to database
  Transmission efficiency comparison between RF model type and CDMA modem
Regular data download for monitoring other sites
4. Ecosystem Monitoring Testbed

## Slide 7
5. Installing Sensor Network
Table 1. Sensor type, Data collection method, and Analysis |  |  | 
Target Place | Sensor type | Data collection method | Analysis
1. Lake Soyang | Troll multiprobe | Real time data transmission | Eutrophication Evaluation
 | (Water temperature, DO, Electrical Conductivity) | RF-modem | 
2. Lake Uiam | combination sensor | Real time data transmission | Eutrophication Evaluation, Turbid water evaluation
 | (Water temperature, DO, Electrical Conductivity, Turbidity) | RF-modem | 
3. Anyang River | Troll multiprobe | Real time data transmission | Analysis of causes of Fish Kill by Oxygen deficit
 | (Water temperature, DO, pH, Electrical Conductivity) | CDMA modem | 
4. Swamp Upo | Hydrolab | Regular download | Eutrophication Evaluation
 | (Water temperature, DO, Electrical Conductivity) |  | 
5. Soyang River | Hydrolab (Water temperature, Electrical Conductivity, Turbidity) | Regular download | Turbid water evaluation
6. Han River | Hydrolab (Water temperature, Electrical Conductivity) | Regular download | Long term Ecological Research, Climate Change,
 |  |  | Eutrophication Evaluation,
7. Gapyeong River | Hydrolab (Water temperature, Electrical Conductivity) | Regular download | Long term Ecological Research, Climate Change

## Slide 8
Troll sensor – DO, turbidity, temp, conductivity per every 5minutes
Buoy platform was installed by K-water
6. Buoy sensor in Lake Soyang

## Slide 9
DO, Temp, turbidity, conductivity sensors
Weekly cleaning of sensors
6. Sensors in Lake Euiam

## Slide 10
sensors installed on a bridge
not connected to internet
Turbidity
DO meter
Controller
Conductivity
battery
6. Sensors in Lake Euiam

## Slide 11
Temperature (Air, Water)
  Thermometer
Dissolved Oxygen(YSI 55)
Turbidity
Conductivity(miniCHEM)
Data logger
DO sensor
Conductivity sensor
Turbidity
sensor
Thermometer
6. Sensors

## Slide 12
7. Expected Effect of KLEON
Community | National Policy
Global Cooperation & IT support Korea : KEON, KLTER, Long Term Ecological Research, K-water Global: GLEON | Environment preservation policy Green Development Pollution prevention
Science | IT
Environment/Ecology Research development (data accumulation & modeling) Improving the accuracy of water quality model Teaching Resource | Real time data management for Ecological Research Data standardization Data integration with Climate data Visualization & Simulation

## Slide 13: Thank You