## Slide 1: Defining cyberinfrastructure for sensor-based environmental observing systems: challenges and opportunities
Sameer Tilak, UCSD
Peter Arzberger, Tony Fountain, Gesuri Ramirez, and Peter Shin

## Slide 2: Outline
Environmental Observing Systems
Streaming Data Middleware
Open Source DataTurbine Overview
Android Sensor Pod
Sensor Network Software O&M
Conclusion

## Slide 3: Observing Systems Approach to Environmental Science
Scientific Grand Challenges
  NRC (National Research Council).
  2001 Grand Challenges in Environmental Sciences
    Biodiversity
    Biogeochemical cycles
    Climate Change
    Hydroecology
    Infectious Disease
    Invasive Species
    Land Use
Comprehensive Approach:
  Real-time multi-resolution observations (sensors, imagery, labs, people)
  Production of quality scientific products (synthesis, modeling, forecasts)
  Collaboration across scientists, programs, agencies, countries

## Slide 4: Observing Systems CI Requirements
Numerous observing systems being planned or built – from local to global
  Ecology, Oceanography, Seismology, Engineering, Hydrology
All have similar CI requirements wrt data acquisition, instrument management, and state-of-health monitoring
  Reliable data capture and transport
  Persistent monitoring of numerous data channels
  Automated processing, event detection, analysis
  Integration across heterogeneous resources and systems
  Real-time tasking and remote operations
  Secure access to system resources
Streaming data middleware provides the framework for application development and integration

## Slide 5: Streaming Data Middleware
Common programming layer for real-time systems
  Enables integration of real-time components
  Provides abstractions over vendor-specific products
  Supports in-network processing (buffering, time synch …)
Make data streams first class objects
  Addressable
  Efficient operations
    Monitoring, QA/QC
    Event detection
    Replication and subscription
    Reliable transport

## Slide 6: Open Source DataTurbine
Open Source Middleware for sensor networks and streaming data applications.
Provides support for integrating heterogeneous sensors and instruments.
Scalable support for in-network intelligent routing, data processing, filtering, and topology management
Originally developed by Creare Inc., http://www.creare.com/
OPEN SOURCE SOFTWARE - Apache 2.0. www.dataturbine.org

## Slide 7: DataTurbine: Generalized Architecture

## Slide 8: RDV – Real-time Data Viewer
Image and video Data
Numeric Data

## Slide 9: DataTurbine GoogleEarth Plug-in
Credit Matt Miller, Creare Inc.

## Slide 10: A Sampler of OSDT Applications
Structural Health Monitoring
Earthquake Engineering
Airborne Environmental Monitoring
Autonomous Vehicles
Coral Reef Monitoring
Shep Pitts, Lotus Engineering and N Carolina State Univ.
Rich Christenson, Univ. of Connecticut
Lawrence C. Freudinger, NASA Dryden Flight Research Center
Russell J. Schmitt, UCSB

## Slide 11
The Open Source DataTurbine (OSDT) Android Sensor Pod: Embedded cyberinfrastructure for smart buoy controllers and experiments in ocean acidification and limnology

## Slide 12: Motivation
Need to replace traditional “dumb” data loggers
Vendor Lock-in
Undocumented interfaces
No support for in-network processing (event detection)
Ad-hoc Remote system (re) configuration and debugging

## Slide 13: Environmental Observing Systems Architecture

## Slide 14: Sensor Network deployment for Biodiversity research
Sensor Selection
Network modality selection
Software Stack Development
  Sensor interface and integration
  Higher-layers (data processing, storage, comm. etc.)
Software configuration
Deployment
Operation and Management
Data Center Component

## Slide 15: Sensor Pod Hardware
Power Supply
Serial to Bluetooth Converters
Solar Panel
Charge Controller
Droid
Phone
Wireless Radio
(shore)
Wireless Radio
(buoy)
Satellite
Modem
Temp., Hum., Volt., Current Sensors
Battery
With 2 batteries the system will remain powered for 8 days without any charge from the solar panels. A complete recharge takes approximately 4 hours depending on solar intensity.

## Slide 16: Android Sensor Pod Architecture
The OSDT Android Sensor Pod includes an integrated suite of software services running on the Android platform. The dtController performs lifecycle management of software services (shown as blue ellipses) running on the Android platform. The DAQ (data acquisition) service is an OSDT source that communicates with sensors and ingests sensor data into OSDT channels (shown as Data In) over Bluetooth. The dtHarvest services multiplex the sensor data into CSV-formatted OSDT channels (shown as Data Out). Various OSDT sink programs (e.g., UDP Caster, UDP Capture, Blue Iridium, and Blue Serial) read the Data Out channels and send data out over multiple radio interfaces.

## Slide 17: XML Configuration and Control
The Sensor Pod can be dynamically reconfigured by modifying a global XML configuration file. Common management tasks can be accomplished efficiently by on-the-fly changes to this file, e.g., adding/removing sensors, changing sample rates, modifying communication policies. This greatly simplifies system configuration and management tasks and enables new science experiments that require real-time adaptive control.
<InstrumentList>
<Instrument>
<name>seaFET</name>
<id>1</id>
<serialnumber>10.0.100</serialnumber>
<imaddress>01</imaddress>
<commandsetlist>
<commandset>
<startdatetime>08/07/2011:10:00:00</startdatetime>
<enddatetime>08/10/201123:00:00</enddatetime>
<frequency>60</frequency>
<command>
<numberofretries>3</numberofretries>
<timeout>40</timeout>
<osdt-server-address>localhost:3333</osdt-server-address>
<osdt-source-name>seaFET01ctd</osdt-source-name>
<osdt-channel-mapping>temp,pressure</channel-mapping>
…
<InstrumentList>
<Instrument>
<name>seaFET</name>
<id>1</id>
<serialnumber>10.0.100</serialnumber>
<imaddress>01</imaddress>
<commandsetlist>
<commandset>
<startdatetime>08/07/2011:10:00:00</startdatetime>
<enddatetime>08/10/201123:00:00</enddatetime>
<frequency>60</frequency>
<command>
<numberofretries>3</numberofretries>
<timeout>40</timeout>
<osdt-server-address>localhost:3333</osdt-server-address>
<osdt-source-name>seaFET01ctd</osdt-source-name>
<osdt-channel-mapping>temp,pressure</channel-mapping>
…
<InstrumentList>
<Instrument>
<name>seaFET</name>
<id>1</id>
<serialnumber>10.0.100</serialnumber>
<imaddress>01</imaddress>
<commandsetlist>
<commandset>
<startdatetime>08/07/2011:10:00:00</startdatetime>
<enddatetime>08/10/201123:00:00</enddatetime>
<frequency>60</frequency>
<command>
<numberofretries>3</numberofretries>
<timeout>40</timeout>
<osdt-server-address>localhost:3333</osdt-server-address>
<osdt-source-name>seaFET01ctd</osdt-source-name>
<osdt-channel-mapping>temp,pressure</channel-mapping>
…
<InstrumentList>
<Instrument>
<name>seaFET</name>
<id>1</id>
<serialnumber>10.0.100</serialnumber>
<imaddress>01</imaddress>
<commandsetlist>
<commandset>
<startdatetime>08/07/2011:10:00:00</startdatetime>
<enddatetime>08/10/201123:00:00</enddatetime>
<frequency>60</frequency>
<command>
<numberofretries>3</numberofretries>
<timeout>40</timeout>
<osdt-server-address>localhost:3333</osdt-server-address>
<osdt-source-name>seaFET01ctd</osdt-source-name>
<osdt-channel-mapping>temp,pressure</channel-mapping>
…
Instrument
Configuration: ID, Serial number, etc.
Commands: start/end time and sampling frequency
Commands: timing information, parsing information, IM address information
DataTurbine related operations: source name, channel names
<InstrumentList>
<Instrument>
<name>seaFET</name>
<id>1</id>
<serialnumber>10.0.100</serialnumber>
<imaddress>01</imaddress>
<commandsetlist>
<commandset>
<startdatetime>08/07/2011:10:00:00</startdatetime>
<enddatetime>08/10/201123:00:00</enddatetime>
<frequency>60</frequency>
<command>
<numberofretries>3</numberofretries>
<timeout>40</timeout>
<osdt-server-address>localhost:3333</osdt-server-address>
<osdt-source-name>seaFET01ctd</osdt-source-name>
<osdt-channel-mapping>temp,pressure</channel-mapping>
…
Instrument
Configuration: ID, Serial number, etc.
Commands: start/end time and sampling frequency
Commands: timing information, parsing information, IM address information
DataTurbine related operations: source name, channel names

## Slide 18: Planned OA Deployments
Palmyra Atoll
Moorea LTER
Martz SeapHox: pH, conductivity, temperature
Pro-Oceanus CO2-Pro: PCO2
MBARI-modified: pH
Sea-Bird Inductive Modem

## Slide 19: Planned Lake Deployment
NTL LTER
Hydro-lab DS-5: chlorophyll, dissolved oxygen
NexSens T-Node: temperature

## Slide 20: Sensor-Rocks: Sensor Network Software O&M Automation
Sameer Tilak and Philip Papadopoulos

## Slide 21: Current Software O&M Approach
The state-of-the-art approach relies on system administrators to build and manage these footprints as golden images that are then burned into similar sensors either in the lab or using Over The Air Programming (OTAP)
Current manual software O&M approach does not guarantee reproducibility and does not scale!

## Slide 22: Motivation: Automating Sensor Device and Network Definition
Inexpensive sensor devices have no interactive screens and must therefore be configured only using a flashed-system image for which there exist only hand-build techniques today for this step
Scaling to 100s or 1000s of sensors means that we must be able to handle hardware heterogeneity of individual sensors without the time-consuming process of building a highly-customized, independent image for each variant; and
We want better reproducibility of the basic software configuration so that we can easily adjust to the rapid changes of the Android environment and reap the benefits of new capabilities.

## Slide 23: Rocks Background
Rocks is a software toolkit that solves the computing cluster definition, deployment and management problem and has reduced the time from raw hardware to a working system within the Data Centers from days/weeks to a few hours.
The toolkit treats a complete software footprint on any machine as a set of software packages and configuration that together form a Rocks Appliance (e.g., database, parallel file servers, load managers, software routers). Appliances can share packages and configuration.

## Slide 24: Data Center Configuration using Rocks
A Portion and a Complete Rocks Config. Graph. Software installation on a given node is performed through the traversal of the configuration graphs.
A Rocks-based sample Data center architecture

## Slide 25: Research Questions
How can you develop a scalable and programmatic mechanism to define software footprint of individual sensors and sensor networks such that it guarantees reproducibility of sensor network cyberinfrastructure?
Can you take a software tool designed to define systems (clusters) in a “friendly” data center environment and scale it down to resource-constrained sensor networks without losing its expressiveness?
Hypothesis: Sensor-Rocks- Modular system footprint construction will become essential as system complexity grows

## Slide 26: Android Software Stack
Android application and kernel stack
key system definition differences between Android
and Full Linux
No scriptable system definition framework like Redhat's Kickstart exists today for Android
Unlike installed Linux systems, common tools for modifying configuration files via scripting languages are not part of the installed Android environmet. This means that Linux can be used to automatically define and configure itself (this is what happens when you install from a DVD)nt, but Android does not have the same closed form.